## Slide 1: ENERGY
Prepared by Dr. Pushpendra rai
Modified by Dr. Druman Utekar

## Slide 2: Energy
The sun, directly or indirectly, is the source of all the energy available on Earth. Energy is essential to life and all living organisms.
Energy is a conserved quantity and the law of conservation of energy states that energy can neither be created nor destroyed but can only be converted from one form to another. The SI unit of energy is Joule.

## Slide 3: Types of Energy

## Slide 4: Classification of Energy

## Slide 5: Distinction: Conventional (non-renewable) and nonconventional energy (renewable) sources.

## Slide 6: Solar Energy
The electromagnetic radiation from sun is commonly known as solar energy. These radiations are
resulted from thermo nuclear fusion reaction on the surface of sun. All the radiation from the sun is not
in the same wavelength range. Almost 92% lie in the range of 315 nm to 1400nm. The estimated
amount of solar flux reaching the atmosphere of earth is approximately 1400W/m2min.and that of heat
equivalent is 2.68 X 1024 J/Year. The eco system of earth utilizes about 0.2-0.5 % of total amount of
solar energy received. It indicates clearly that large amount solar energy get wasted, which otherwise
can be immense use for satisfying needs of humans.
Advantage of solar energy:
1. It is non-polluting and non-depleting source of energy.
2. It is renewable source of energy.
3. It is available abundantly.
In spite of these advantages, the use of solar energy in large scale is still not in practice, due to
following reasons,
1. Non availability of intense light in all areas throughout year
2. Difficulties faced in economic collection and conversion of solar energy into other forms of
energy such as electricity.
The solar energy has been successfully used in following purpose
i) Heating: Used for water and space heating in colder countries.
ii) Electricity: Using solar energy electric energy can be generated.

## Slide 7: Advantages and Disadvantages

## Slide 8: Solar Water Heater

## Slide 9
Flat Plate Collector:
The device works on the principle of black body in which heat absorbing capacity and tendency of a black surface is utilized to achieve benefits for human.
Construction:
These are the main components of a typical flat-plate solar collector:
 Black surface - absorbent of the incident solar energy
 Glazing cover - a transparent layer that transmits radiation to the absorber, but prevents radiative
and convective heat loss from the surface
 Tubes containing heating fluid to transfer the heat from the collector
 Support structure to protect the components and hold them in place
 Insulation covering sides and bottom of the collector to reduce heat losses
Application
Some advantages of the flat-plate collectors are that they are:Easy to manufacture
 Low cost, Collect both beam and diffuse radiation
 Permanently fixed (no sophisticated positioning or tracking equipment is required)
 Little maintenance

## Slide 10: PHOTO VOTAIC CELL (SOLAR CELL) A conventional solar cell structure is shown in figure:
Semiconductors like silicon has the capacity to absorb light and deliver a portion of the energy of the
absorbed photons to carry charge carriers (electrons and hole).Thus solar cell is a semiconductor
diode that has been designed carefully so that it can absorb the light energy efficiently and convert
light energy from the sun into electrical energy.

## Slide 11
Construction: A typical silicon photo voltaic cell composed of thin layer of phosphorus doped
silicon (n-type) on top of boron doped (p-type) silicon. Hence these two layers form p-n junction. A
metallic grid is the electrical contact of the diode and allows light to fall on the semiconductor
between the grid lines. An anti-reflective layer between the grid lines increases the amount of light
transmitted to semiconductor.
Working: of tiny energy packets called photon. When light radiation falls on the p-n junction diode,
photons are absorbed and electron-hole pairs are generated. The electrons are diffused and collected
at the n-type end and holes are diffused and collected at the p-type end. When these two ends are
electrically connected through a conductor, there is a flow of current between the two ends through
the external circuit. Thus photoelectric current is produced and available for use. The current output
of a cell depends on its efficiency and size and is proportional to the intensity of sun light striking the
surface of the cell. Therefore, photovoltaic cells are connected electrically in series or parallel circuits to produce higher voltages, currents and power levels. A number of solar cells electrically connected
to each other and mounted in a support structure or frame is called a photovoltaic module. A
photovoltaic array is the complete power generating unit, consisting of any number of photovoltaic
modules and panels.

## Slide 12: Advantages & Disadvantages

## Slide 13: Fuel cells
H2-O2 fuel cells-Self Study

## Slide 14: Fuels
Fuels can be defined as substances which undergo combustion in the presence of air to produce a large amount of heat that can be used economically for domestic and industrial purpose.
Examples, Wood, Coal, Kerosene, Petrol

## Slide 15: Classification of chemical fuels
Based on the origin: i) Primary or natural fuels
ii) Secondary or artificial or derived fuels
B) Based on Physical State: i) Solid Fuels
ii) Liquid Fuels
iii) Gaseous Fuels
C) Based on Chemical Nature
Organic eg. Vegetable fuel, coal
Inorganic eg. Iron Pyrites
Nuclear Fuels eg. Uranium oxide

## Slide 16: Characteristic Properties of Fuels
Fuels are characterized by testing certain physical and chemical properties.
Calorific Value should be as high as possible.
Ignition temperature-Moderate
Flame temperature should be as high as possible.
Flash and Fire point should be as high as possible.
Aniline point should be low.
Cloud and Pour point should be as low as possible.
Viscosity should be adequate.
Coke number should be as high as possible.
Moisture content-as low as possible.
Volatile matter as low as possible.
Ash content should be absent.
Easy risk free transport should be possible.
Storage space-ideally fuel should occupy small space.
Air requirement- adequate
Harmless products should be produced on combustion.

## Slide 17: Calorific Value
Calorific value is defined as the number of parts of water which gets heated through 1°C by the heat evolved by the complete combustion of one unit weight of fuel( unit volume of gaseous fuels) under the conditions such as
Whole of heat evolved is absorbed by water.
The products formed leave the system at atmospheric temperature and pressure.
It is the most important property of fuel.

## Slide 18: Units of calorific value
B.T.U. (British Thermal Unit)
A British thermal unit may be defined as the heat required to raise the temperature of one pound of water from 60°F to 61°F.
2) K.C.U. (Kilogram Centigrade Unit)
The calorie, a unit of heat may be defined as, the heat required to raise the temperature of one Kg of water from 15°C to 16°C.
Correlation between BTU and KCU:
1BTU = 0.252KCal =252Cal
1KCal = 3.968 BTU
3) C.H.U. (Centigrade Heat Unit)
The calorific value can also be expressed as centigrade heat unit (C.H.U.)., which is the amount of heat required to raise temperature of one pound of water through one degree centigrade.

## Slide 19
1) High Calorific value (HCV) or Gross Calorific value (GCV):
High calorific value may be defined as the total amount of heat produced when one unit of the fuel has been burnt completely and the products of combustion have been cooled to 16°C or 60°F.
2) Low calorific value( LCV) or Net Calorific value (NCV)
Low calorific value may be defined as the net heat produced when unit mass or volume of fuel is completely burnt and products are allowed to escape.
NCV or LCV = GCV (HCV) – Latent Heat of water formed
= GCV(HCV) – Mass of hydrogen x 9 x Latent heat of steam
= GCV(HCV) – 0.09 x %H x 587
Because 1 part by weight of hydrogen produces 9 parts (1+8) by mass of water.

## Slide 20: Dulong Formula
The calorific value of fuels is determined theoretically by Dulong formula or I.A. Davies formula.
It is expressed as
Q = 1/100 [ 8080 x C + 34500 x (H – O/8) + 2240 x S]
Where, Q = Calorific value in KCU/Kg
C = % of carbon
H = % of hydrogen
O = % of oxygen
S = % of sulphur
Dulong formula for HCV & LCV
HCV = 1/100 [8080 x C + 34500 x (H – O/8) + 2240 x S]
LCV = HCV –[ 9/100 x %H x 587]
Experimentally calorific value of solid and liquid fuel is determined using Bomb Calorimeter.

## Slide 21
Numerical 1: A sample of coal contains C = 55%, O = 28%, H =7%, S = 0.7%, N =0.2%, Ash = 0.2%. Calculate the GCV and NCV.
Soln:
GCV = 1/100[ 8080C + 34500(H-O/8) + 2240S]
= 1/100 [ 8080x55 + 34500(7-28/8) + 2240 x 0.7]
= 5667 Kcal/Kg
NCV = HCV – 0.09 x % H x 587
= 5667 – 0.09 x 7 x 587
= 5297.19Kcal/Kg
Numerical 2: A sample of coal has following composition C = 70%, O = 8%, H = 10%, N =3%, S = 2%, Ash = 7%. Calculate HCV and GCV.
Numerical 3: A sample of coal contains C = 61% , O = 32%, S = 0.5%, N = 0.2% and Ash = 0.3%. If NCV of coal is 5313.02KCal/Kg. Calculate % H and GCV.
GCV =1/100[8080C + 34500(H-O/8) + 2240S]----i)
NCV = GCV -0.09x%Hx587
GCV = NCV + 0.09x%H x587-------ii)
1/100[8080C + 34500(H-O/8) + 2240S) = NCV + 0.09x%Hx587

## Slide 22
Numerical 3: A sample of coal contains C = 61% , O = 32%, S = 0.5%, N = 0.2% and Ash = 0.3%. If NCV of coal is 5313.02KCal/Kg. Calculate % H and GCV.
GCV =1/100[8080C + 34500(H-O/8) + 2240S]----i)
NCV = GCV -0.09x%Hx587
GCV = NCV + 0.09x%H x587-------ii)
1/100[8080C + 34500(H-O/8) + 2240S) = NCV + 0.09x%Hx587

## Slide 23
Numerical 3: A sample of coal contains C = 70% , O = 25%, S = 1%, N = 1% and Ash = 0.5%. If NCV of coal is 5200KCal/Kg. Calculate % H and GCV.
GCV =80.80x70 + 345(H-25/8) + 22.40x1]----i)
=5656+345H-1078.125+22.4
= 4600+345H
NCV = GCV - 0.09x%Hx587
GCV = 5200 + 0.09x%H x587
= 5200 + 52.83H-------ii)
4600.275+345H = 5200 + 52.83H
345H- 52.83H = 5200-4600.275
292.17H = 599.725
H = 2.05%
GCV= 5308.44Kcal/Kg

## Slide 24: Coal
Purpose of Analysis of Coal
To decide price of coal
To determine quality
To specify use of coal for a particular purpose.
To calculate theoretical calorific value of coal.
To calculate air requirement for complete combustion of coal and design the furnace fire box suitably.

## Slide 25
Types of Analysis of Coal
Proximate Analysis
% Moisture
% Volatile Matter
% Ash
Fixed Carbon
B) Ultimate Analysis
% Carbon and % Hydrogen
% Nitrogen
% Sulphur
% Ash

## Slide 26: Proximate Analysis of Coal
Proximate analysis is the study or analysis of coal sample in which
% Moisture b) % VM c) % Ash d) % Fixed Carbon are found out.
a) % Moisture
A known weight of powdered and air dried coal sample is taken in a crucible and it is places in an oven for 1hr at 110°C. Then the coal is cooled in a desiccator and weighed out. If the initial weight of the coal is W gms and final weight is W1 gms.
Then the loss in weight (W-W1) corresponds to moisture in coal.
% Moisture = Loss in weight x 100 = (W-W1) x 100
Weight of coal sample W

## Slide 27
b) % Volatile Matter
Moisture free coal left in the crucible in first experiment W1 is covered with a lid loosely. Then it is heated at 925°C in a muffle furnace for 7min.
The crucible is taken out and cooled in a desiccator. Then it is weighed (W2 gms) .
% Volatile matter = weight of volatile matter x 100 = (W1-W2) x100
Weight of coal sample W
c) % Ash
The residual coal in the above experiments is heated and burnt in an open crucible at above 750°C for half hour.
The coal gets burnt. The ash left in crucible is cooled in a desiccator and weighed W3 gms.
% Ash = weight of ash x 100 = W3 x 100
Weight of coal W
d) % Fixed Carbon:
It is found by calculations
%FC = 100-[% moisture + % VM + % Ash)

## Slide 28
Significance or Importance of proximate analysis
Moisture
It decreases calorific value of coal largely as it does not burn and takes away heat in the form of latent heat.
It increases ignition point of coal.
Hence a coal with lower moisture % is better quality.
b) Volatile matter
It decreases calorific value of coal.
It elongates flame and decreases flame temperature.
It form smoke and pollute air.
However the coals containing 15-25% of VM on carbonization gives coke oven gas which is source of various organic aromatic chemicals.
Such coal have good coaking property and coke can be obtained from the coals.
Overall regarding burning of coal the coal with lesser VM is better quality coal.
c) Ash
It reduces calorific value of coal as ash is non-burning part in coal.
Ash disposal is a problem.
Ash fuses to form clinker at high temperature obstructing the air supply of coal burning furnace.
Hence lesser the % ash better is the quality of coal.
d) Fixed carbon
Carbon is the burning part in coal and higher the fixed carbon higher is calorific value.
Hence a good quality coal contains high fixed carbon percentage.

## Slide 29
Numerical 1: A sample of coal was analysed for content of moisture, volatile matter & ash. From the following data, calculate the percentage of the above quantities.
i) weight of coal taken = 2.5g
ii) weight of coal after heating ar 110°C = 2.365g
iii) weight of coal after heating at covered crucible at 950°C = 1.165g
iv) constant weight obtained at the end of the experiment = 0.460g
Soln:
% Moisture = (W-W1) x 100 = ( 2.5-2.365 )x 100 =5.4%
W 2.5
b) % volatile Matter = (W1-W2)x 100 = (2.365-1.165) x 100 = 48%
W 2.5
c) % Ash = W3 x 100 = 0.460 x 100 = 18.4%
W 2.5
d) % Fixed Carbon = 100 – [% moisture + % VM + % Ash]
= 100 – [5.4 + 48+ 18.4] = 28.2%

## Slide 30: Ultimate Analysis
1) Carbon and 2) hydrogen:
About 1-2 g of accurately weighed coal sample is burnt in a current of oxygen in a combustion apparatus. C and H of the coal are converted into CO2 and H2O respectively. The gaseous products of combustion are absorbed respectively in KOH and CaCl2 tubes of known weights.
The increase in weights of these are then determined.
C + O2 ----->CO2
2H2 + O2-----> 2H2O
KOH + CO2-----> K2CO3 + H2O
CaCl2 + 7 H2O-----> CaCl2.7 H2O

## Slide 31
3) Nitrogen by Kjeldahl’s Method: About 1 g of accurately weighed powdered 'coal is heated with concentrated H2SO4 along-with K2SO4(catalyst) in a long-necked flask(called Kjeldahl’s flask). After the solution becomes clear, it is treated with excess of KOH and the liberated ammonia is distilled over and absorbed in a known volume of standard acid solution. The unused acid is then determined by back titration with standard KOH solution. From the volume of acid used by ammonia liberated, the percentage of N in coal is calculated as:

## Slide 34
Numerical 1: 0.2g of Coal Sample is accurately weighed and is burnt in a combustion apparatus. The gaseous products of combustion are absorbed in potash bulb and calcium chloride tubes of known weights. The increase in weight of potash bulb and CaCl2 tube are 0.66g and 0.08g respectively. Calculate the % C and % H in coal sample.
Numerical 2: 3g of coal was heated in Kjeldahls flask and NH3 gas evolved was absorbed in 40mL of 0.5N HCl. After absorption the excess acid required 18.5mL of 0.5N KOH for exact neutralization. 2.3g of coal sample in quantitative analysis gave 0.35g BaSO4. Calculate % of N and S in coal sample.
Soln: Volume of NH3 consumed by 0.5N HCl is in terms of 0.5N KOH
40ml of 0.5N HCl = 40mL of 0.5N KOH---assumed---V1___blank
Unreacted acid = 18.5ml of 0.5N KOH----V2____back titration
Vol of acid reacted with absorbed NH3 in term of 0.5N KOH = 40 – 18.5ml = 21.5mL
% N = volume of acid consumed(V1-V2) x N KOH x 1.4
weight of coal sample
% S = Wt of BaSO4 formed x 32x 100
wt of coal sample x 233
Numerical 3: 2.5 g of coal was heated in Kjeldahls flask and NH3 gas evolved was absorbed in 40mL of 0.5 N HCl. After absorption the excess acid required 8.5mL of 0.25N KOH for exact neutralization.
Soln:
Blank titration = 40mL of 0.5N HCl = 40mL of 0.5N KOH
Back titration = 8.5mL of 0.25N KOH = __4.25__ml of 0.5N KOH----n1v1=n2v2

## Slide 36: SECONDARY BATTERIES

## Slide 37: INTRODUCTION
Rechargeable batteries (also known as secondary cells) are batteries that potentially consist of reversible cell reactions that allow them to recharge, or regain their cell potential, through the work done by passing currents of electricity.

## Slide 38: working
Rechargeable (or secondary) batteries contain active materials that can be regenerated by charging. All batteries have positive and negative terminals, marked (+) and (-) respectively, and two corresponding electrodes. The electrodes must not touch each other, and are separated by the electrolyte, which facilitates the flow of electric charge between the electrodes. A collector conducts the charge to the battery's exterior and through the load.

## Slide 39
When a battery is inserted into an electrical device, the device completes the circuit between the two terminals and triggers electrochemical reactions within the battery. The anode undergoes an oxidation reaction with the electrolyte and releases electrons, while the cathode undergoes a reduction reaction and absorbs the free electrons. The product of these two reactions is electricity, which is channeled out of the battery and into the device.

## Slide 40
When a secondary battery is recharged, its electrodes undergo an opposite process to the discharging action described above. As the battery charger passes electricity through the battery, its cathode is oxidized and produces electrons which are then absorbed by the anode. When the battery is fully charged, it can be connected to a load and discharged again.

## Slide 41: Working(charging)

## Slide 42
Types Of Secondary Batteries
lead–acid battery
nickel–cadimium battery
lithium-ion battery

## Slide 43: 1.Lead acid Batteries

## Slide 44
1 Chemistry of a Lead Acid Battery
2 Composition of a Lead Acid Battery Positive Plate: Lead Oxide (PbO)
Negative Plate: Lead (Pb)
Electrolyte: sulphuric acid (H2SO4)
3 Review of Acid Terminology Strong vs. Weak Acids
Strong acids completely ionize in water
EX: HCl  H+ + Cl- (HCl + H2O  H3O+ + Cl-)
Weak acids partially ionize in water
EX: HC2H3O2 ⇌ H+ + C2H3O2-
(note ⇌ versus ) Monoprotic vs. Diprotic Acids
Monoprotic acid has one H+ (EX: HCl)
Diprotic acid has two H+ (EX: H2SO4)

## Slide 45
4 The Electrolyte: H2SO4
H2SO4 is classified as a strong acid (completely ionizes) but that is not exactly true. The first ionization of H2SO4 is complete and occurs instantly when in water.
EX: H2SO4  H+ + HSO4-
But! The second ionization is extremely partial.
EX: HSO4- ⇌ H+ + SO4-2 (Ka = 0.012!)
This is very important in understanding the chemistry of a lead acid battery!
5 for understanding
In general, is sulfuric acid considered a strong or weak acid?
Strong- Why is sulfuric acid considered to be strong?
It completely ionizes
What ion related to sulfuric acid is weak?
HSO4̶- Why is the bisulfate ion, HSO4̶ considered weak?
It partially ionizes

## Slide 46
6 Lead Acid Batteries are rechargable This leads to two different sets of redox reactions.
The discharging phase. The charging phase.
7 Chemistry of Discharge Phase Negative plate reaction (oxidation):
Pb + HSO4̶  PbSO4 + H e̶
Positive plate reaction (reduction):
PbO2 + HSO4̶ + 3H+ + 2e-  PbSO4 + 2H2O
Overall discharge redox reaction:
Pb + PbO2 + 2 HSO4̶ + 2H+  2 PbSO4 + 2H2O
or…Pb + PbO2 + 2 H2SO4  2 PbSO4 + 2H2O
Note: states are removed for simplicity
Pb, PbO2, and PbSO4 are always solids
HSO4-, H+, and H2SO4 are always aqueous
H2O is always a liquid

## Slide 47
8 The flow of electrons = ELECTRICITY!
9 Chemistry of Charge Phase Negative plate reaction (reduction):
PbSO4 + H e-  Pb + HSO4̶
Positive plate reaction (oxidation):
PbSO4 + 2H2O  PbO2 + HSO4̶ H+ + 2e-
Overall charge redox reaction:
2 PbSO4 + 2H2O  Pb + PbO2 + 2 HSO4̶ + 2H+
or…2 PbSO4 + 2H2O  Pb + PbO2 + 2 H2SO4
10 for understanding
What metal is always at the negative plate? Pb
What compound is always at the positive plate? PbO2
What is the electrolyte in a battery? H2SO4 or HSO4̶
What compound is the “waste” product of discharge and has to be removed in the charging process? (think!) PbSO4

## Slide 48
11 Why do batteries “die”?
Dead Battery
New Battery When the battery discharges solid PbSO4 is formed.
In a new battery, the PbSO4 is in a spongy form which can easily be converted back to Pb and PbO2.
Over time the PbSO4 will tend to crystallize.
The crystallized PbSO4 cannot be converted back to Pb and PbO2 so there is not only less reactant material but it also coats the surface of the Pb and PbO2.
New Battery
Dead Battery
The combined equation for both the processes is represented as

## Slide 49
Life
The optimum functional temperature for lead acid battery is 250C which means 770F. The increase in the range of temperature shortens longevity. A per the rule, for every 80oC increase in temperature, it reduces the half-life of the battery. While a value regulated battery that functions at 250C has a lead acid battery life of 10 years. And when this is operated at 330C, it has a life period of 5 years only.
Lead Acid Battery Applications
These are employed in emergency lightening to provide power for sump pumps.
Used in electric motors
Submarines
Nuclear submarines

## Slide 50: INTRODUCTION
The nickel–cadmium battery is a type of rechargeable battery using nickel oxide hydroxide and metallic cadmium as electrodes. Ni-Cd batteries are made in a wide range of sizes and capacities.
Nickel(hydroxide)–cadmium systems are the most common small rechargeable battery type for portable appliances. The sealed cells are equipped with “jelly roll” electrodes, which allow high current to be delivered in an efficient way. These batteries are capable of delivering exceptionally high currents, can be rapidly recharged hundreds of times, and are tolerant of abuse such as over discharging or overcharging.
It produces a voltage of about 1.4 V
2. NICKEL-CADMIUM BATTERY

## Slide 51: INVENTIONS AND SCOPE
Nickel-cadmium (NiCd)
Invented by Waldemar Jungner in 1899. Developments were slow, but in 1932, advancements were made to deposit the active materials inside a porous nickel-plated electrode. Further improvements occurred in 1947 by absorbing the gases generated during charge, which led to the modern sealed NiCd battery.
For many years, NiCd was the preferred battery choice for two-way radios, emergency medical equipment, professional video cameras and power tools. In the late 1980s, the ultra-high capacity NiCd rocked the world with capacities that were up to 60 percent higher than the standard NiCd.
Since the disposal of battery is hazardous to environment alternative cells are being used such as paper battery

## Slide 52: RECENT TRENDS
The primary trade-off with Ni–Cd batteries is their higher cost and the use of cadmium. This heavy metal is an environmental hazard, and is highly toxic to all higher forms of batteries.
Recently, nickel–metal hydride and lithium-ionbatteries have become commercially available and cheaper, the former type now rivaling Ni–Cd batteries in cost..
The batteries are more difficult to damage than other batteries, tolerating deep discharge for long periods.
Ni–Cd batteries typically last longer, in terms of number of charge/discharge cycles, than other rechargeable batteries such as lead/acid batteries.
Compared to lead–acid batteries, Ni–Cd batteries have a much higher energy density.
In consumer applications, Ni–Cd batteries compete directly with alkaline batteries. A Ni–Cd cell has a lower capacity than that of an equivalent alkaline cell, and costs more.
The capacity of a Ni–Cd battery is not significantly affected by very high discharge currents.

## Slide 53: CELL REPRESENTATION AND CELL REACTION
A typical Ni-Cd battery is represented as
Cd| Cd(OH)2|| NiO(OH)| Ni(OH)2
Cell reaction while discharging
At Anode: oxidation of Cd metal
Cd + 2OH_ Cd(OH)2 + 2e-
At cathode: reduction of NiO(OH)
2NiO(OH) + 2H2O + 2e- 2Ni(OH)2 + 2OH-
Net Cell reaction:
2NiO(OH) + 2H2O + Cd 2Ni(OH)2 + Cd(OH)2

## Slide 54: ADVANTAGES
Fast and simple charging process
It is compact and lighter than traditional batteries
It has a longer life than lead storage batteries
Available in a wide range of sizes and performance options
Good low-temperature performance
Only battery that can be ultra-fast charged with little stress

## Slide 55: LIMITATIONS
It is rather more expensive than a lead storage battery
It has a lower energy density value
Cadmium is a toxic metal. Cannot be disposed of in landfills
Memory effect; needs periodic full discharges
High self-discharge; needs recharging after storage

## Slide 56: APPLICATIONS
Ni-Cd cells are popularly used in many appliances because they are available in variety of sizes and capaciities.
Few examples are:
Calculators
Electronic flash units
Transistors
Cordless appliances

## Slide 57: 3. RECHARGEABLE LITHIUM Batteries

## Slide 58: DESCRIPTION
A lithium-ion battery or Li-ion battery (abbreviated as LIB) is a type of rechargeable battery in which lithium ions move from the negative electrode to the positive electrode during discharge and back when charging.
The electrolyte, which allows for ionic movement, and the two electrodes are the constituent components of a lithium-ion battery cell.

## Slide 59: Electrolytes
Role-
Ion conduction between cathode and anode.
They are generally, Lithium salts dissolved in organic solvent.
Commercial electrolytes: in Carbonate solvent.

## Slide 60: Anode Materials
Requirements:
Large capabilites of adsorption.
High efficency of charge/discharge.
Low reactivity against electrolyte.
Fast reaction rate.
Low cost
Environment friendly
Commercial anode materials:
Hard Carbon, Graphite

## Slide 61: Cathode Materials
Requirements:
A high discharge voltage
A high energy capacity
A high power density
Light weight
Low self discharge
Environment friendly
Commercial cathode materials:
LiCoO2, LiFePO4 etc.

## Slide 62: Chemical Reactions
Main essential components...
Anode: Graphite [carbon] - C(s)
Cathode: Lithium Cobalt Oxide - LiCoO2
Electrolyte: Typically a combination of lithium salts - LiPF6, LiBF4, or LiClO4, in an organic solvent, such as either.
Separator: The separator is a very thin sheet of micro perforated plastic. - CH2=CHCl

## Slide 63: Reactions while charging
On charge the positive electrode, cathode, material is oxidized, Li+ ions are de-intercalated from the layered lithium LiCoO2, pass across the electrolyte and are intercalated between the graphite layers in graphite by an electrochemical reduction reaction proceeding at the negative electrode.

## Slide 64: Reactions while discharging
When the cell is discharged, an oxidation reaction occurs at the negative electrode, Li+ ions are de-intercalated from the anode and migrate across the electrolyte to be re-intercalated into the cathode material, due to charge balance the equivalent number of electrons travel through the external circuit. A simultaneous electrochemical reduction reaction proceeds at the positive electrode and accepts electrons from the external circuit, Li+ ions from the electrolyte, to reform the starting material. A change from electronic current to ionic current occurs at the electrode/electrolyte interface.

## Slide 66: Applications
Emergency Power Backup Or UPS
Dependable Electric And Recreational Vehicle Power
Solar Power Storage
Reliable And Lightweight Marine Performance
Solar Power Storage
Surveillance Or Alarm Systems In Remote Locations
Personal Freedom With Mobility Equipment
Portable Power Packs That Eliminate Downtime

## Slide 68: Waste to energy conversion

## Slide 69: Waste to Energy
The increasing industrialization, urbanization and changes in the pattern of life give rise to generation of increasing quantities of wastes.
Scarcity of fossil fuels particularly petroleum crude is forcing us to develop some clean technology for the utilization of the fossil fuels as well as to utilize renewal resources.
In recent years, technologies have been developed that not only help in generating substantial quantity of decentralized energy but also in reducing the quantity of waste for its safe disposal.

## Slide 70: Types of waste
There are different types of waste which are generated from our daily or industrial activities such as organic waste, e-waste, hazardous waste, inert waste etc.
Organic waste refers to waste which degrades or broken down by microorganisms over time. All organic wastes are essentially carbon based compounds.
Organic waste has significant portion in overall waste generation in industrial/urban/ agricultural sector and therefore it can be used for energy generation.

## Slide 72: Important Parameters of different types of waste
Solid Waste | Waste Water | Waste Gas
Elemental Composition C, H, N, O & S | BOD & TOC | Particulate Matter
Moisture, Volatile & Ash content | pH, | Nox, Sox and CO
Bulk Density, | TDS and TSS | Heavy metal ions
Heating Value | Cations and anions | Hydrocarbon and other fuel
Hence the factors like Carbon content of solid waste , BOD and sludge content of liquid fuels and Combustible gas content of gaseous waste are important parameters for converting waste in to energy. |  | 

## Slide 73: Composition of Municipal Waste
Chart: % Composition
| Bio degradable | Recyclable | Inorganic | Others
% Compo | 50 | 22 | 20 | 8

## Slide 74: Need for energy production from waste
Waste to energy conversion gives the following advantages
1) It meets some energy demand, on the other way it gives some a systematic solid waste management system.
2) It helps us to achieve the sustainability goal of the society,
3) Decrease in production of green house gases
4) Reduction of dependance on fossils fuels
5) Waste to energy technology converts municipal waste into electric, heat and fuels
6) Reduction of waste going to land fills

## Slide 75: Methods of production of energy from waste
1. Incineration: incineration is a waste treatment process that involves the combustion of organic substances content in waste materials
2. Gasification: gasification is a process that converts carbonaceous feedstocks into combustible gasses including H2 and CO mainly carbon monoxide and hydrogen dioxide gas.
3. Pyrolysis: pyro means fire, lysis means cutting. So, this is the process that is thermal decomposition process which decomposes carbonaceous material by the application of heat in absence of oxygen.
4. Anerobic Digestion: In an oxygen-free tank, this material is broken down to biogas and fertilizer.
In incineration we used excess amount of oxygen in gasification we use controlled amount of oxygen and in pyrolysis we use no oxygen theoretically.

## Slide 76: E-waste
Electronic waste or E-waste describes the discarded electrical or electronic devices.
Sources of e-waste
Waste produced due to data generating & processing devices like computers, monitors, speakers,keyboards, printers etc.
Electronic devices used in TV, DVDs and CDs.
Equipment's used in communication like phones, landlines phones, mobiles etc.
Household equipment like vacum cleaner, microwave ovens, washing machines, air conditioners etc

## Slide 77: Effect of e-waste on environment
Emission from e-waste create environmental damage
Toxic chemicals from e-waste enter into soil-crop-food pathway.
They are non-biodegradable causing pollution of soil
E-waste dumping yards causes pollution and health hazards.
It cause health hazards due to lead, mercury, cadmium poisoning

## Slide 78: E-wate management
Common methods
Landfill disposal
Incineration
Acid treatment
Advanced method
Recycling
It involves
Disassembling-carefully separating various components
Upgrading-involves mechanical or chemical or metallurgical methods to recover the metals
Glass, plastic, metals can be recovered and then mixed with other ingredients to produced many valuable recycled products.

## Slide 79
Thank you